## Slide 1
Achieving Results Faster, Together

## Slide 2: Getting prepared – Project Operations Manual and Data Requirements
Achieving Results Faster, Together
Session # D.4
UNDERSTANDING THE ROLE OF DIGITAL INFRASTRUCTURE

## Slide 3: Enhance understanding of data requirements for ASCENT carbon activities and identify challenges and mitigation strategies to support effective implementation.
Achieving Results Faster, Together
Session Objective

## Slide 4: What data collection and management practices are put in place as part of the ASCENT Energy Access Program and how that could be leveraged for the ASCENT Carbon Program? What kind of arrangements are put in place to collect data from project developers? Are there any data privacy/licensing concerns to be aware of?
Achieving Results Faster, Together
Before We Start..

## Slide 5: Why Program Operations Manual (POM)?
Why this manual? Establishes minimum MRV requirements so emission reductions are real, measurable, additional and conservative across ASCENT cookstoves, SHS, mini‑grids, and grid extension. Provides a modular framework that countries can use for different technologies, with harmonized data systems and verification cycles. Core Objective Define institutional roles & responsibilities for the carbon component Specify baseline, activity, and monitoring datasets and schedules. Set QA/QC controls (SOPs, back‑checks, error handling). Align with emerging dMRV protocols and recognized standards. ASCENT ecosystem alignment Aligns with ASCENT program purpose, regional platform and d‑MRV emphasis via COMESA & partners. Requirements under the Energy Access standard and GCC ASCENT Energy Access portal.
Achieving Results Faster, Together

## Slide 6: POM Content Overview & Roles and Responsibilities
What the POM covers Core Framework — Institutional arrangements; MRV workflow from data collection → QA/QC → Annual Monitoring Reporting (AMR) → verification. Technology Modules —Cookstoves; SHS; mini‑grids; grid extension (baseline/activity/monitoring tables, parameters, frequencies). Annexes — Survey/KPT ToRs, distribution/installation templates, sampling guidance (90/10)
Key roles (illustrative highlights) Project Implementing Unit (PIU) — Owns the central MRV database, compiles AMR, conducts QA/QC oversight. Participating Organizations (POs) — Primary data collection (installations, IDs, PAYGo/meter logs, surveys) and completeness. Utilities/Operators — New connections, billing/consumption data, uptime logs. Independent Verification Agent (IVA)/VVB — Desk/phone/field checks; statistical sampling (e.g., 90/10) and real time monitoring.
Achieving Results Faster, Together

## Slide 7: Data To Collect (Examples for Two Technologies)
Grid Extension Baseline: Pre‑connection energy situation (none/diesel/mini-grid) — one‑time survey or official studies. Activity: Unique meter/connection ID (or GPS); connection type (HH/non‑HH); connection date; end‑user info; carbon waiver form. Monitoring: Metered kWh per connection (monthly/annual); grid emission factor (annual); grid uptime (operator logs). Method notes: Grid emission factor (EF) computed per UNFCCC grid tool or country data; ensure consistent EF source & year. B. Improved Biomass Cookstoves Baseline: Fuel use and cooking patterns (surveys/official reports/Kitchen Performance Test-KPT) and HH size. Activity: Stove model, unique ID, distribution/installation dates, end‑user info, carbon waiver. Monitoring: Usage/stacking (surveys, optionally stove use monitors - SUMs), fuel consumption (KPT), HH size updates. Method notes: Favor direct measurement where feasible (SUMs, metered fuel/energy). KPT v4.0 provides field protocol; SUMs provide objective usage and stacking evidence.
Achieving Results Faster, Together

## Slide 8: QA/QC Procedures and Verification Approach
Built‑in QA/QC (at PIU & implementer levels) SOPs for surveys, device tagging, data entry; digital tools where possible (e‑surveys, smart meters, PAYGo integrations). Back‑checks/audits on 5–10% (depends) of samples; validation of digital logs vs. ground truth; automated error flagging for missing/implausible values/duplicates; enumerator training & refreshers. Data governance: central database, secure transfer, versioning, audit trails; annual QA/QC summary in AMR. Verification (IVA/VVB) Desk (consistency/completeness), phone, field checks scheduled to align with issuance cycles (annual/biennial). Sampling design to meet 90/10 confidence/precision (UNFCCC small‑scale sampling guidance) and to minimize bias (seasonality, attrition).
Achieving Results Faster, Together

## Slide 9: Anticipated Data Collection Challenges (and some practical mitigations)
Stove usage & stacking uncertainty (self‑report bias; Hawthorne effect) → Mitigate with: SUMs on sub‑samples; KPT with digital scales; usage caps & cross‑checks per Energy Access Standard; stratified sampling; clear user/non‑user definitions. Baseline fuel & fNRB controversy (key driver of emission reductions) → Mitigate with: MoFuSS or conservative defaults where required; transparent references; regular methodological updates. Household attrition & panel maintenance (lost contact, migration) → Mitigate with: Oversampling buffers; updated contact/GPS at install; phone survey protocols; replacement rules; panel refresh schedules aligned to issuance cycles. Utility billing quality & meter data gaps (Grid Extension/Mini‑grids) → Mitigate with: Automated data feeds, revenue‑grade metering, meter health checks, exception dashboards; formal data‑sharing MoUs with utilities; backstop surveys if gaps persist.
Achieving Results Faster, Together

## Slide 10: Anticipated Data Collection Challenges (and some practical mitigations)
Sampling & seasonality bias → Mitigate with: Pre‑calculated sample sizes for 90/10; stratify by geography / season / implementer; document assumptions; keep chain‑of‑custody for all instruments and survey data. Grid emission factor availability → Mitigate with: Adopt UNFCCC Grid Tool, or credible national EF series; archive sources yearly; note corrections. Validator capacity for dMRV → Mitigate with: Early engagement of accredited VVBs and targeted training plan (with the support of COMESA/GCC).
Achieving Results Faster, Together

## Slide 11: Discussion
What other data collection and management challenges you anticipate and any resource constraints we should be aware of?
Are there any data privacy/licensing concerns to be aware of?
Where the most of capacity challenges exist?
Achieving Results Faster, Together

## Slide 12
Achieving Results Faster, Together